## Slide 1
The Odds Booster
ECE445 Final Presentation
Tim Green, Jack Arndt, Marco Rojas
05/02/2022

## Slide 2
Objective
Problem + Solution
Ethical Considerations
Design & Construction
System Overview
Subsystems
Implementation
Successes & Challenges
Demonstration Video
Subsystems
Conclusion
Wrap Up
Redesign Considerations
Further Work
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
OVERVIEW
2

## Slide 3
OBJECTIVE
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING

## Slide 4
The Problem:
Casino Games are intimidating to new players
People currently tend to learn these games only from playing with peers
Easy to lose money if you don't know the best strategies
Our Solution:
Teach players how to play the game and the best move for each situation
Provide these benefits in the context of a physical game
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
OBJECTIVE
4
The Odds Booster high-level usage diagram

## Slide 5
Cheating
  RFID Tags – No Casino Usage
  Public Knowledge
Gambling
  This device only assists players desiring to play these games
  No actual gambling required
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
ETHICAL CONSIDERATIONS
5
Our cards with RFID tags shown in center

## Slide 6
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
DESIGN & CONSTRUCTION

## Slide 7
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
SYSTEM BLOCK DIAGRAM
7

## Slide 8
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
POWER SUBSYSTEM – BATTERY
Considerations
Output voltage (3.3V & 9.6V)
Maximum current required (~1.08A)
Features
Output voltage (4.2V - 3.0V)
Continuous discharge current (1.5A)
Estimated worst-case battery life (2.78hrs)
Battery protection circuitry included
8
Mikroe-4474 Li-Polymer Battery

## Slide 9
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
POWER SUBSYSTEM – POWER TREE
Considerations + Features
High current capabilities
Adjustable output voltage
Large heat sink (LDO)
Current sensing + limiting (Buck)
Complex switching controllers (Boost & Buck)
Requirements
Drop from 3.3V - 3.7V to 3.3V. When below 3.3V, match the input voltage.
Reliably step-up voltage from 3.7V to 9.6V
Step-down voltage from 5V (USB) to 4.2V
9
Power Subsystem Block Diagram

## Slide 10
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
CARD READER SUBSYSTEM
Considerations + Features
3.3V input
Automatic MCU interface detection
13.56MHz frequency standard
Solderable package
Price ($24.28)
Requirements
RFID Tags on each playing card must work reliably
Receive 13.56MHz RFID signals at antenna
Ensure functional matching network
Transmit RFID signals to MCU
10
Card Reader Subsystem Block Diagram

## Slide 11
Considerations + Features
2.4GHz antenna in module
UART interface for coding and debugging
High clock rate
Significant documentation and examples
Reset debouncing circuitry
Requirements
Transmit and Receive Bluetooth packets at a distance of 3ft and average throughput of 5kbps.
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
COMMUNICATIONS SUBSYSTEM
11
Communications Subsystem Block Diagram

## Slide 12
Considerations + Features
VGA style control
Picture quality (320x240 with 24-bit color depth)
Price ($11.53)
Connector availability
Requirements
MCU generates 6.5MHz clock and 52MHz clock
Output display data to GPIO pins serially at 52MHz
MCU write to PSRAM frame buffer while displaying screen
GRAINGER ENGINEERING
DISPLAY SUBSYSTEM
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
12
Display Subsystem Block Diagram

## Slide 13
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APP SUBSYSTEM
Considerations + Features
C++ language of choice
Blackjack game of choice
Text-based GUI
Requirements
The app uses Bluetooth to send/receive data with MCU
The app uses card information to accurate calculate optimal decisions
The app displays the measures and suggestions in the form of text
13
Wait
Receive new card
Update game status
End of Initial Dealing?
No
Calculate optimal decision(s), display to user
Receive user action
Yes
End of hand?
Reset game status
Yes
No
App flowchart diagram

## Slide 14
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
FINAL IMPLEMENTATION
Physical Implementation
PCB Layout
14

## Slide 15
SUCCESSES & CHALLENGES
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING

## Slide 16
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
VIDEO SIMULATION – BLUETOOTH CONNECTION & BLACKJACK GAMES
16

## Slide 17
Requirements/Verifications
Battery protection
LDO drops voltage to 3.3V
Boost steps up voltage to 9.6V
Buck steps down voltage to 4.2V
Results
LDO successful operation (see graph)
Boost successful operation (9.6V output)
Buck unsuccessful (2mV output)
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
POWER SUBSYSTEM
17

## Slide 18
Challenges
Buck MOSFET gate control signals
Buck soldering challenges
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
POWER SUBSYSTEM
18
Buck device's duty cycle gate signals
Buck device shown under screwdriver head

## Slide 19
Requirements/Verifications
RFID Tags on each playing card must work reliably
Receive 13.56MHz RFID signals at antenna
Ensure functional matching network
Transmit RFID signals to MCU
Results
Successful RFID tag readings
Command register output (xBF) --> NCS Pin Issue
  Failure to correctly interface with MCU
Challenges
"0" Nets
MCU parallel interface detection
Lack of common use (no outside help)
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
CARD READER SUBSYSTEM
19
Command register description
Connection scheme for detecting the parallel interface type

## Slide 20
Requirements/Verifications
Must use Bluetooth to communicate with app at a 3ft distance at 5kbps
Results
Average 5kB file transfer rate: 17.136kbps
Challenges
Classic Bluetooth vs Bluetooth LE
GPIO-12 pull-down and flash initialization to 3.3V
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
COMMUNICATIONS SUBSYSTEM
20
Tested Bluetooth throughput: 21.6kbps

## Slide 21
Requirements/Verifications
MCU must generate both 6.5MHz and 52MHz clock signals
MCU must output the screen data serially to 3 GPIO pins at 52MHz
MCU must write to external PSRAM
Results
Pixel Clock – 6.7MHz
H-Sync – 16.34kHz
V-Sync – 62Hz
Data – 3.35MHz (or off)
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
DISPLAY SUBSYSTEM
21
Pixel Clock Output Signal
V-Sync (Screen Refresh) Output Signal

## Slide 22
Challenges
Maximum clock output capabilities
Control interface implementation (I2S Parallel)
Frame buffer allocation and DMA data
Backlight theories and pin switch
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
DISPLAY SUBSYSTEM
22
Switched VDD/GND Pins
Backlight unit testing on separate board

## Slide 23
Requirements/Verifications
The app utilizes Bluetooth to send/receive data with MCU
The app uses card information to accurate calculate optimal decisions
The app displays the measures and suggestions in the form of text
Results
Functionality shown in demo video
Challenges
Classic Bluetooth vs Bluetooth LE
Socket Programming
Hand Count for a single player with splitting
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APP SUBSYSTEM
23
GUI suggesting user to "double" in given hand of blackjack

## Slide 24
CONCLUSION
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING

## Slide 25
HARDWARE
Successful power tree
  LDO/Boost
Physical playing card deck
Proper LCD signals
UART MCU programming & execution
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
PROJECT ACCOMPLISHMENTS
SOFTWARE
Functional Bluetooth communication
Text-based GUI
Accurate game suggestions
  Blackjack
25

## Slide 26
HARDWARE ISSUES
Controller for LCD
  GPIO Pins, RAM, Reliability
MFRC531 complications
Native phone capabilities
USER ISSUES
Soldering considerations
  Buck & Antenna placement
Spare parts – LCD Connector Replacement
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
REDESIGN CONSIDERATIONS
26

## Slide 27
SOFTWARE IMPROVEMENTS
Using previous hand knowledge
Blackjack custom rules & further optimizations
Texas Hold'em suggestion implementations
Machine learning
PHYSICAL/HARDWARE
Packaging
Antenna design
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
FURTHER WORK
27

## Slide 28
Thank you for watching!
Questions?
The Odds Booster
Team 37
Tim Green, Jack Arndt, Marco Rojas
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING

## Slide 30
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX A: SCHEMATICS
LDO Schematic
Boost Schematic

## Slide 31
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX A: SCHEMATICS
Buck Schematic
Card Reader Schematic

## Slide 32
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX A: SCHEMATICS
Communication/MCU Schematic
LCD Schematic

## Slide 33
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX B: CHARTS/DATASHEETS
Chosen blackjack strategy
MFRC531: StartUp phase procedure
MFRC531: Separate Read/Write strobe timing diagram

## Slide 34
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX B: CHARTS/DATASHEETS
MFRC-MCU Interfacing Issue
MFRC531 "0" Nets

## Slide 35
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX B: CHARTS/DATASHEETS
LCD 52MHz Clock Signal Impossibility
Fully specific block diagram

## Slide 36
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
APPENDIX B: CHARTS/DATASHEETS
Limited MCU DRAM

## Slide 37
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
Slide Title

## Slide 38
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
Slide Title

## Slide 39
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
Slide Title

## Slide 40
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
Slide Title

## Slide 41
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
Slide Title

## Slide 42
CHART / GRAPH
(Short commentary or relevant information about the contents of the chart/graph.)
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING
Slide Title

## Slide 43
IMAGE (Send to back so Block I is not covered.)
(Text here relevant to the photo for a larger call out on a given idea or message.)
(Keep this text simple and short on one or two lines.)
ECE445 – SENIOR DESIGN LAB – FINAL PRESENTATION
GRAINGER ENGINEERING